## Slide 1
AMRITA RACING
Telemetry & Data Visualization System
Turning Sensor Data into Readable, Usable Information
Phase 1 — Data & Sensor Planning
Vehicle Dynamics / Controls & Electronics

## Slide 2
Why This Project
The problem we're solving
Data without meaning
Every session our sensors will record thousands of raw readings — voltages, angles, pressures, speeds. On its own, that data tells us nothing.
No way to read it
Right now there is no system to turn that raw data into something the team can actually look at and understand.
What we need
A tool — app / software — that takes live sensor data from the car and converts it into clear graphs and readings for every subsystem.
Amrita Racing | Telemetry & Data Visualization — Phase 1
2

## Slide 3
Phase 1 Approach
How this list was put together
1
Reviewed the full car documentation
Technical Vehicle System Documentation (TVSD) and the Vehicle Dynamics Instrumentation Roadmap — every subsystem, front to back.
2
Listed every useful calculation / graph
Subsystem by subsystem — acceleration, battery, braking, suspension, electronics, and more.
3
Reverse-mapped each calculation to variables
For every graph, identified exactly which physical quantities need to be measured to produce it.
4
Matched variables to sensor types
Marked what's already on the car and what still needs to be procured.
Amrita Racing | Telemetry & Data Visualization — Phase 1
3

## Slide 4
Calculations & Graphs Overview
Count of planned calculations / graphs, by subsystem
Subsystem | # of Calcs / Graphs
Vehicle Dynamics (general) | 22
Tractive System / HV Battery | 18
Suspension | 14
Brakes | 11
Drivetrain | 10
Steering | 7
Motor & Motor Controller | 7
Tyres | 7
Lap Time & Performance | 7
Low Voltage / Electronics (CES) | 8
Aerodynamics | 5
Driver Inputs | 5
Chassis / Structural | 4
Thermal / Cooling | 3
Environment | 3
131
total calculations
/ graphs planned
Full list with descriptions and required
sensor variables is in the companion
Excel sheet.
Amrita Racing | Telemetry & Data Visualization — Phase 1
4

## Slide 5
Examples: Vehicle Dynamics & Mechanical
A few flagship graphs from each area — full list in the Excel sheet
Vehicle Dynamics
G-G diagram (friction circle usage)
Understeer gradient (steering vs lateral g)
Roll & pitch gradient vs g
Suspension
Damper velocity histogram (per corner)
Motion ratio verification
Ride height / roll trace
Brakes
Brake bias ratio vs time
Brake disc temperature vs time
Wheel lock-up detection
Drivetrain
Wheel speed & slip ratio
Motor RPM vs torque
Drivetrain efficiency (wheel power / motor power)
Amrita Racing | Telemetry & Data Visualization — Phase 1
5

## Slide 6
Examples: Tractive System, Electronics, Aero & Driver
A few flagship graphs from each area — full list in the Excel sheet
Tractive System (HV Battery)
Pack voltage, current & power vs time
State of charge & cell voltage spread
Insulation resistance (safety monitoring)
Low Voltage / Electronics
Fault event log (AMS / IMD / BSPD / SCS)
LV rail voltage stability
Shutdown circuit state timeline
Aerodynamics & Tyres
Airspeed vs GPS ground speed
Tyre pressure & temperature vs time
Tyre slip angle vs lateral force
Driver Inputs
Combined throttle + brake + steering trace
Throttle / brake overlap check
Lap time & sector comparison
Amrita Racing | Telemetry & Data Visualization — Phase 1
6

## Slide 7
Minimum Necessary Sensors — Start Here
To avoid blowing the budget immediately, procurement is split into priority tiers
Tier 1 — Already Required / Near-Zero Extra Cost
6-axis IMU, GPS(already installed)
Brake pressure transducers, F & R (rule-required)
Current sensor + voltage transducer (rule-required HV monitoring)
BMS — per-cell voltage & temperature (already on car)
Insulation Monitoring Device (already on car)
Dual APPS pedal sensors (rule-required)
Motor & controller data via CAN — no new hardware
4x wheel speed sensor — only genuinely new item, and low-cost
What Tier 1 Already Unlocks
Speed, lap time & sector comparison
G-G diagram / longitudinal & lateral acceleration
Brake bias ratio & pressure vs deceleration
Wheel lock-up detection
Pack voltage, current, power & SOC vs time
Cell voltage spread & insulation resistance (safety)
Fault event log & APPS plausibility check
Motor RPM / torque vs time
Nearly all Tier 1 sensors are already required for the car to run safely — this gives us a full working telemetry system before we spend anything new.
Amrita Racing | Telemetry & Data Visualization — Phase 1
7

## Slide 8
Sensor Requirements Summary
Key sensors needed, by subsystem — with rollout priority
Subsystem | Key Sensors Needed | Priority
Vehicle Dynamics | 6-axis IMU, GPS receiver | Tier 1 — Now
Brakes (pressure & pedal) | 2x brake pressure transducer, pedal position pot | Tier 1 — Now
Tractive System (HV) | 2x current sensor, 2x voltage transducer, BMS, IMD | Tier 1 — Now
Motor & Controller | Dual APPS pedal sensor, motor/controller data via CAN | Tier 1 — Now
Wheels / Drivetrain | 4x wheel speed sensor (Hall / IR) | Tier 2 — Next
Suspension | 4x string pot / LVDT (wheel & damper travel) | Tier 2 — Next
Steering | Steering angle sensor | Tier 2 — Next
Brakes (thermal) | 4x brake disc IR temperature sensor | Tier 2 — Next
LV / Electronics | LV branch current monitors | Tier 2 — Next
Tyres | 4x TPMS pressure sensor, 4x IR tyre temperature sensor | Tier 3 — Later
Aerodynamics | Pitot tube + differential pressure sensor | Tier 3 — Later
Chassis | Strain gauges at key structural nodes | Tier 3 — Later
Environment | Ambient temp/humidity sensor, barometric pressure sensor | Tier 3 — Later
Amrita Racing | Telemetry & Data Visualization — Phase 1
8

## Slide 9
Phased Procurement Plan
Buy only what's necessary first — expand gradually as budget allows
TIER 1 — NOW
Already on the car / near-zero cost
IMU, GPS
Brake pressure transducers
Current sensor (DHAB S/118)
Voltage transducer (LV 25-P)
BMS (Orion Jr BMS 2)
Insulation Monitoring Device
Dual APPS sensors
Motor/controller CAN data
→
TIER 2 — NEXT
Buy once Tier 1 is validated
4x suspension string pot / LVDT
Steering angle sensor
4x brake disc IR temp sensor
LV branch current sensors
4x wheel speed sensors
→
TIER 3 — LATER
Future expansion, as budget allows
4x TPMS tyre pressure sensor
4x tyre IR temperature sensor
Pitot tube + pressure sensor
Strain gauges (chassis)
Ambient temp / humidity sensor
Barometric pressure sensor
Pedal load cell
This phased approach avoids a large upfront spend while still building a fully working telemetry system from day one.
Amrita Racing | Telemetry & Data Visualization — Phase 1
9

## Slide 10
This data lets us properly read what's happening
in the car during live testing —
and use it to make real, informed improvements to the car.
AMRITA RACING

## Slide 11
Questions & Discussion
Amrita Racing | Telemetry & Data Visualization — Phase 1